Part-1

---
PA current source

---
Part-2

---
Circuit
- Cascode amplifier combines a common source(M1) and a common gate stage (cascode device, M2).
- They are used in operational amplifiers that implement very large voltage gains and in precision current mirrors.
- The resistance looking into drain of cascode device M2 is quite high.
- The overall gain of the circuit is given as:
  - gm,1*ro,1*gm,2*ro,2
{g_{m,2}}*{r_{o2}}*{r_{o,1}}

---
Layout generation
- Layout of parameterized cascode common source
- DRC
- LVS

---
Ngspice testbench

---
Simulation testbench